## Slide 1: IP Integrator and IP Catalog
Artix-7
Vivado 2014.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Achieve greater design productivity using Vivado IP Integrator
  Rapidly create and reuse subsystem level IP with Vivado and IP Integrator
  Describe the IP Packager features
  Differentiate between the free and evaluation base IP available in IP Catalog
  Use the Clocking Wizard to configure and add clocking resources to the design

## Slide 3: Outline
IP Integrator
IP Packager
IP Catalog
Clocking Wizard
Summary

## Slide 4: Challenges of Designing with Complex IP
Modern IP contains multiple complex interfaces
  Many signals, complex port mappings in RTL
  Connectivity in overall design not apparent
Modern IP is highly parameterizable
  Designer must maintain consistency between interconnected IP blocks
  Designer must understand interactions between blocks
Subsystems containing multiple IP blocks are often difficult to capture and reuse
  How to best capture IP for reuse
To help designers be more productive when integrating IP, Xilinx introduced the IP Integrator in the Vivado Design Suite

## Slide 5: What is IP Integrator?
A hierarchical IP integration tool for processor based and non-processor based systems
A graphical and scriptable IP configuration and connection environment
IP Integrator
IP Usage
Extensible IP Catalog
IP Management and Delivery
IP Repository
Integrated Design Environment
IP Packager

## Slide 6: Benefits of Vivado IP Integrator
Interface Level Connectivity
  Connect complex interfaces between IP in a single step
  Users can create custom interface definitions
Integration and Reuse of IP
  Rapid creation of complex IP by packaging the contents of a diagram
Automatic Generation of HDL
  Instantiates all IP in a diagram and makes all the interconnections
Take advantage of IP metadata
  Propagate correct parameters to connected IP
  Recognition of unique data types
Processor based system support
IP Integrator
IP Usage
Extensible IP Catalog
IP Management and Delivery
IP Repository
Integrated Design Environment
IP Packager

## Slide 7: Vivado IP Integrator User Interface
Interface Connections with Live DRCs
System Hierarchy View
TCL Console
Hierarchy Support
Extensible IP Repository
Notes: Many of the advanced feature of IP Integrator are highlighted here. Beginning in the upper left, all of the IP sources and resulting HDL generated from a diagram are shown in the Vivado sources window. IP Integrator does not generate separate project files, so integration issues are nonexistent.
When making connections between blocks, DRC are run real time. These DRCs show the designer the valid connection possibilities, and do not allow improper connections.
IP Integrator supports arbitrary levels of hierarchy. It is very easy to place a related group of IPs into a new level of hierarchy, and equally easy to break the hierarchy if needed.
A simple right click on a diagram opens the searchable IP Catalog, allowing any IP to be quickly added to a diagram.
Finally, every graphical action has a corresponding Tcl command that is run. The Tcl console updates for each action. A special Tcl command is available that will generate a complete script that can be used to recreate any diagram, including parameter settings on IP.

## Slide 8: Intelligent IP Integration: Correct by Construction Design
Real-time DRCs
Default width=32
Is updated to
propagated value
IP2
IP1
IP0
User specifies width=64
Input width=64
after propagation
IP2
AXIS Width Converter
IP0
User specifies
width=64
IP1
IP2 only supports
width=32
Parameter Propagation
Parameter Resolution
Auto Connection
Apply solution 1
Notes: The real time DRCs that run will alert the designer to errors that may exist in a diagram. DRCs can be run at any time to provide feedback. In some cases, IP Integrator can alert the user to a problem and provide an automated means to correct the problem.
Some IP is almost always connected to other IP in a standard way. In this case, IP can contain automation rules that will handle adding and connecting the other IP. An example of this is MicroBlaze. If a MicroBlaze is in a design, there is almost always local BRAM memory, a reset block, possible a DDR memory controller, and common peripherals. When the MicroBlaze is added to a diagram, the user is alerted to the fact that automation rules exist for MicroBlaze. If the user chooses to run the rules, a dialog will open prompting the user to answer some questions, and then IP Integrator will add and connect the other IP.
Parameter propagation is one of the most power features available in IP Integrator. IP can be packaged with specific propagation and design rules, and IP Integrator will run these rules as the diagram is created. For example, IP0 is added to a diagram, and by default, has a 64 bit wide data bus. IP1 is then added and connected, as is IP2. In this case, IP2 has a default databus width of 32 bits. When the parameter propagation rules are run, the user is alerted to the fact that IP2 has a different bus width. Assuming that the data bus width of IP2 can be changed through a change of parameter, IP Integrator can automatically update IP2. This is a simple example, but demonstrates the power of parameter propagation. The types of errors that can be corrected by parameter propagation are often errors not found until simulation.
If an IP does not support changing of a certain parameter, IP Integrator can sometimes resolve the incompatibility using parameter resolution. For example, different bus widths can be fixed by the automatic addition of a bus width converter. Active signal levels can be resolved by auto insertion of inverters.

## Slide 9: Outline
IP Integrator
IP Packager
IP Catalog
Clocking Wizard
Summary

## Slide 10: Reusing Your IP
IP from many sources can be packaged and made available in Vivado
All IP available in the Vivado IP Catalog can be used to create IP Integrator designs
Any IP Integrator diagram can be quickly packaged as a single complex IP
IP Packager
Source (C, RTL, IP, etc)
Simulation Models
Documentation
Example Designs
Test Bench
Vivado IP Integrator
Standardized IP-XACT representation
IP Catalog
Xilinx IP
3rd Party IP
User IP
Notes: Vivado supports reuse of IP is by providing users a means to capture their individual IP or IP subsystems and package that IP, and then make the IP available to other users through the Vivado IP catalog. This approach also benefits third party IP providers, who now have a standard way of providing their IP for both evaluation and purchase, and that IP will be visible through the IP Catalog.
Packaging an IP Integrator diagram takes one Tcl command, or several mouse clicks.

## Slide 11: Capture Your IP Using the Vivado IP Packager
Wizard-based flow
  Automates generation of IP-XACT IPs
  Many pieces of meta-data automatically inferred
  Users can add additional meta-data
Notes: Vivado IP Packager is a powerful wizard built into Vivado that guides the user through the necessary steps of packaging IP. Xilinx uses an industry standard method of capturing IP sources, metadata, constraints, and documentation – that method is commonly called IP –XACT. Users can package HDL source or netlists, and once packaged, add them to repositories that can be visible to other designers.

## Slide 12: Customizing IP for Reuse in IP Packager
Add, Edit or change defaults
Select
Options
Notes: The packager handles all the IP-XACT specific file creation, manages IP versions, recognizes interfaces, and creates customized configuration dialogs, as well as more advanced functionality.

## Slide 13: Using and Reusing Packaged IP
The Vivado IP Catalog can be extended by adding additional IP Repositories. Third party IP, your custom IP, and Xilinx provided IP are displayed in the identical manner

## Slide 14: IP Packager
The IP Packager allows a core to be packaged and included in the IP Catalog, or for distribution
Complete set of files include
  Source code, Constraints, Test Benches (simulation files), documentation
IP Packager can be run from Vivado on the current project, or on a specified directory

## Slide 15
IP Packager
Automatically analyze project/files to determine parameters
Initial Summary
Identifies
  Files
  Parameters
  Ports
  Interfaces
Creates GUI Layout for IPI

## Slide 16: IP Packager
Modify configuration
  Properties
  Compatibility
  Files
  Custom parameters
  Ports
  Interfaces
  Address and Memory
  IP and security

## Slide 17: IP Repository
Creates .xml file for the IP
Specify the directory in the repository
Displays IP in the repository

## Slide 18: Outline
IP Integrator
IP Packager
IP Catalog
Clocking Wizard
Summary

## Slide 19: IP Catalog
The IP Catalog contain a collection of IP that can be used to assemble a system
Supported by IPI
Facilitates quick system construction
Each IP block has its own configuration parameters
Most of the IP are free, some require licenses
Stored as source code in the install directory
  Always synthesized with the latest tools
  Some proprietary source code is encrypted

## Slide 20: Vivado IP Catalog
Integrated IP Support
  Instant access to IP customization
  Vivado IP GUI look and feel
  Support for Vivado synthesis and implementation
  Selectable IP output products
  Full Tcl support
Notes: Vivado has a unified IP catalog – all IP available in one place. The catalog can be extended through use of additional repositories. IP can be selected in the catalog and customization GUIs launched. IP is then added directly to a Vivado project, or in the case of IP Integrator, added to the diagram. The user can select simulation or implementation files. IP can be accessed and customized entirely from the Tcl console as well.

## Slide 21: Peripheral and Non-Peripheral Type IP
Many IP in the catalog are peripheral type
  Peripheral type are indicated by AXI4, AXI4-Stream
Non-peripheral IP listing do not have entry in the ACXI4 column
Status column indicates if the IP is of production or pre-production category
License column indicates if the IP is free (Included) or costs money (Purchase)

## Slide 22: IP Peripherals Included as Source (Free)
Bus and bridge controllers
Debug cores
DMA and Timers
Inter-processor communication
External peripheral controller Memory and memory controller
High-speed and low-speed communication peripherals
Other cores

## Slide 23: IP Cores Included as Evaluation
AXI CAN controller
AXI USB2 device
Video IP
Telecoms/ Wireless IP
Xilinx developed, delivered, and supported
Evaluation IP installs with a 90-day evaluation license

## Slide 24: IP Cores
Right click to customize
Determine compatibility
Product Guide (datasheet) > Document Navigator
Change Log
Product Webpage
Answer record
Export complete IP Catalog to excel

## Slide 25: Outline
IP Integrator
IP Packager
IP Catalog
Clocking Wizard
Summary

## Slide 26: Clocking Resources: MMCM and PLL
Up to 24 CMTs per device
One MMCM and one PLL per CMT
Two software primitives (instantiation)
  *_BASE has only the basic ports
  *_ADV provides access to all ports
PLL is primarily intended for use with the I/O phaser for high-speed memory controllers
The MMCM is the primary clock resource for user clocks

## Slide 27: Inference
Clock networks are represented by nets in your RTL design
  The mapping of an RTL net to a clock network is managed by using the appropriate clock buffer to generate that net
Certain resources can be inferred
  A primary input net (with or without an IBUF instantiated) will be mapped to a global clock if it drives the clock inputs of clocked resources
    The BUFG will be inferred
  BUFH drivers will be inferred whenever a global clock (driven by a BUFG) is required in a clock region
    BUFHs for each region required will be inferred
BUFIO, BUFR, and BUFMR cannot be inferred
  Instantiating these buffers tells the tools that you want to use the corresponding clock networks
PLLs and MMCMs cannot be inferred

## Slide 28: Instantiation
All clocking resources can be directly instantiated in your RTL code
  Simulation models exist for all resources
  Refer to the Library Guide for HDL Designs
  Use the Language Templates ( ) tab
PLLs and MMCMs have many inputs and outputs, as well as many attributes
  Optimal dividers for obtaining the desired characteristics may be hard to derive
  The Clocking Wizard via the IP Catalog
    Only *_ADV available

## Slide 29: Invoking Clocking Wizard
Click on the IP Catalog
Expand FPGA Features and Design > Clocking
Double-click on Clocking Wizard
The Clocking Wizard walks you through the generation of complete clocking subsystems

## Slide 30: The Clocking Wizard: Clocking Options
Select Primitives to be used
  MMCME2_ADV
  PLLE2_ADV
Specify the primary input frequency and source type
  Optionally, select and specify secondary input clock
Select clocking features
  Frequency synthesis
  Phase alignment
  Dynamic phase shift
  …

## Slide 31: The Clocking Wizard: Output Clocks
Select the desired number of output clocks
Set the desired output frequencies
Select optional ports

## Slide 32: The Clocking Wizard: MMCM Settings
Allows overriding of wizard settings
Sets the phase, period, jitter…

## Slide 33: The Clocking Wizard: Port Renaming
Change input/output port names
Change optional port names

## Slide 34: The Clocking Wizard: Summary
Shows the input, output frequencies
Other attributes depending on the selections made
The Resource tab on the left provides summary of type and number of resources used

## Slide 35: Generating Output Products
Generate Instantiation Template
Synthesis model
Simulation model
Implementation related files
Examples on how to use the product
Optionally, synthesized design checkpoint so it can be used in the implementation without re-synthesizing in the project

## Slide 36: Outline
IP Integrator
IP Packager
IP Catalog
Clocking Wizard
Summary

## Slide 37: Summary
Vivado is an IP Centric design environment, allowing multiple ways to add/manage IP
  Automatic RTL generation
  Rapid assembly, packaging, and reuse of IP subsystems
  Processor based system design support
Vivado IP Integrator provides unique time to market advantages when designing with complex IP
The IP Packagers provides flexibility of IP reuse and repackaging
The IP Catalog provides access to extensive IP resources
  Simple IP to highly complex IP
  Grouped according to functionality
The Clocking Wizard enables the configuration of complex clocking resources